## Slide 1: Preparing…
Click on all icons

## Slide 2: Attitude and Orbit Determination and Control of Small Satellites
Politecnico di Torino
Electronics Department
Space Avionics Technology Center
Leonardo M. Reyneri
Politecnico di Torino
Electronics Department

## Slide 3: PART I
Satellite Orbits and Localization

## Slide 4: Spacecraft Orbits
Int’l Space Station (ISS) orbiting Earth
By NASA - http://spaceflight.nasa.gov/gallery/images/shuttle/sts-130/html/s130e012142.html, Public Domain, https://commons.wikimedia.org/w/index.php?curid=9537591

## Slide 5: Spacecraft Orbits
Soyuz TMA-7 orbiting Earth
By The original uploader was Thegreenj at English Wikipedia - Transferred from en.wikipedia to Commons., Public Domain, https://commons.wikimedia.org/w/index.php?curid=2726282

## Slide 6: Spacecraft Orbits
Two bodies of different mass orbiting a common barycenter
By User:Zhatt - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=280053

## Slide 7: Spacecraft Orbits
Newton's cannonball – how speed affects orbit:
A,B: too slow!
C: critical speed
D: elliptical
E: too fast!
By user:Brian Brondel - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=1657849

## Slide 8: Circular Orbit
V
Fg
Fv
R
Ms
Me
(equilibrium)

## Slide 9: Circular Orbit
V
Fg
Fv
R
NO gravity!
Re
h

## Slide 10: Circular Orbit
V
Re
h
!!!
Me

## Slide 11: Circular Orbit
Low Earth Orbit
(200-2000) km
Medium Earth Orbit (2000-35,786) km
High Earth Orbit
> 35,786 km
GEO
(23 h 56 min 4 s)

## Slide 12: Elliptical Orbit
V
R
Me
For circular ():
A
perigee
apogee
Ms

## Slide 13: Orbital params (Keplerian elements)
Rp
Ra
Perigee/periapsis
Apogee/apoapsis
Eccentricity:
2) Semi-major axis:
A

## Slide 14: Orbital params (Keplerian elements)
Reference plane: Earth Equatorial plane
Reference direction: First Point of Aries
1) Eccentricity e
2) Semi-major axis a
By Lasunncty at the English language Wikipedia, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=8971052

## Slide 15: Orbital params (Keplerian elements)
3) Inclination w.r.t. Reference plane
4) Longitude of ascending node w.r.t. Reference direction
5) Argument of perigee w.r.t. Ascending node

## Slide 16: Orbital params (Keplerian elements)
6) True anomaly w.r.t. perigee.
It is the only time-varying element!

## Slide 17: Orbit Inclinations
Equatorial: inclination
Polar Prograde: inclination but
Polar Retrograde: inclination but
Equatorial Retrograde: inclination
Sun Synchronous: polar retrograde (around ) such that the satellite passes over any given point of the planet's surface at the same local solar time.

## Slide 18: Orbital manoeuvres
V
Re
h
Change orbit altitude and/or eccentricity
Change orbital plane (, , )
Formation flight: very frequent (or continuous) very little manoeuvres to keep relative distance w.r.t. another spacecraft. It is very much mission-dependent

## Slide 19: Circular  Elliptical Orbit
Start from circular (, )
Then apply such as:
R
Me
A
V1

## Slide 20: Circular  Elliptical Orbit
Vo+ΔV
R
Me
A*
For ΔV=0, it remains circular:
V1

## Slide 21: Elliptical  Circular Orbit
Apply another such that:
Orbit returns circular!
BUT, we have changed orbit radius!
R*
Me
V1
V1+ΔV

## Slide 22: Formation Flight
Formation flight = mantaining a constant relative position among a set of spacecraft.
Many alternatives. A few cases:
Along same orbit (in sequence on the same orbit). In theory the simplest, but…
Along same orbital radius (same orbital period, different altitudes)
Along parallel orbits (same orbital period, same altitude)

## Slide 23: Formation Flight
Re
h1
Me
h2

## Slide 24: Formation Flight

## Slide 25: Propulsion
Problem: we have to apply a . How ?
Newton’s laws:
Preservation of momentum: if : = const if : … = const if : = 0
Force Impulse: if we apply for :

## Slide 26: `Propulsion
How to apply a ?
Must apply a single force Requires either:
A “fixed point” from which to apply a momentum (i.e. to exert a force for a given time ):
Find a source of «pressure» on a «sail» of surface (e.g. solar light)

## Slide 27: Orbital Manoeuvres
Ejecting mass (usually a gas) at a high speed (from 0 to ) to preserve total momentum:
Gas speed is usually expressed by means of the “specific impulse” (seconds)

## Slide 28: An Exercise - I
Given a spacecraft with mass on circular LEO with altitude
Compute spacecraft speed
Compute orbit period
Compute to transfer spacecraft into an elliptical orbit with apogee altitude
Compute to transfer spacecraft into an circular orbit with altitude

## Slide 29: Answers - I
Spacecraft speed
Orbit period
First orbit manoeuvre
Second orbit manoeuvre

## Slide 30: An Exercise - II
Compute time to achieve using only solar pressure () on a sail of
Compute gas mass to achieve knowing gas speed ()
Compute to maintain formation flight with at altitude for mission duration

## Slide 31: Answers - II
Time
Gas mass
Required

## Slide 32: Thrusters
Rockets
Specific impulse
Viking 5C rocket engine
By Sanjay Acharya - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=4293802

## Slide 33: Thrusters
Gridded ion thrusters
Specific impulse
By Oona Räisänen - Own work; self made in Inkscape. Based on File:Ion_engine.gif., CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=20308289

## Slide 34: Thrusters
Hall-effect thrusters
Specific impulse
By Dstaack at English Wikipedia - Transferred from en.wikipedia to Commons., Public Domain, https://commons.wikimedia.org/w/index.php?curid=2137404

## Slide 35: Thrusters
Cold Gas thrusters
Specific impulse
http://www.cubesat-propulsion.com/jpl-marco-micro-propulsion-system/
http://www.cubesat-propulsion.com/reaction-control-propulsion-module/

## Slide 36: Solar Sails
By Andrzej Mirecki - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=14656159
IKAROS spaceprobe
14m x 14m solar sail
2kg mass
1mN thrust

## Slide 37: Thrusters for CubeSats
http://www.cubesat-propulsion.com/vacco-systems/

## Slide 38: Center Of Gravity (C.O.G.)
What point of a spacecraft exactly remains on the orbit and exactly follows the rules of gravity?
The so-called CENTER OF GRAVITY (C.O.G.)
The most important points for orbit and attitude evaluation and control !!!
It is very important to be able to compute its position on-board spacecraft

## Slide 39: Center Of Gravity (C.O.G.)
C.O.G. is a point C; it has coordinates (X,Y,Z) w.r.t. geometrical center of satellite.
Each coordinate (X/Y/Z) is the weighted mean of the corresponding coordinate of each subsystem:

## Slide 40: An Exercise - III
Imagine a 1U CubeSat (10cmx10cmx10cm) with:
six walls of 100g each located 5cm from geometrical center
One power supply unit of 150g located at coordinate (0,0,+4cm) w.r.t. geometrical center
One on-board computer of 80g located at coordinate (0,0,+3cm) w.r.t. geometrical center
One payload of 250g located at coordinate (1cm,-2cm,-1cm) w.r.t. geometrical center
What is the total mass and where is located C.O.G. ?

## Slide 43: An Exercise - III
Lateral panels:
W1: 100g (0,0,+5cm)
W2: 100g (0,0,-5cm)
W3, W4…

## Slide 44
X
Z

## Slide 45
X
Y

## Slide 46: An Exercise - III
Lateral panels:
W1: 100g (0,0,+5cm)
W2: 100g (0,0,-5cm)
W3, W4… 100g (…,…,…)
Other subsystems:
Power supply: 150g (0,0,+4cm)
OBC: 80g (0,0,+3cm)
Payload: 250g (1cm,-2cm,-1cm)

## Slide 47: Answers III
Total mass is
C.O.G. is located at (0.23cm,-0.46cm,+0.55cm)

## Slide 48: Satellite Position and Orbit
Spacecraft Position is position of center of gravity at any given instant
Spacecraft Orbit is the set of all consecutive positions and is independent of time
In reality spacecraft orbit slowly varies with time because of several perturbations
48
Earth
P(t)
O

## Slide 49: Effects of Position in Orbit
Day & night…
Earth
P(t)
O
SUN

## Slide 50: Effects of Position in Orbit

## Slide 51: Effects of Position in Orbit
Magnetic field…
O
P(t)

## Slide 52: Effects of Position in Orbit
Magnetic field…

## Slide 53: Effects of orbit altitude
Van Hallen Belts are two zones of energetic charged particles, most of which originate from the solar wind that is captured by and held around Earth by its magnetic field.
By Booyabazooka at English Wikipedia - Transferred from en.wikipedia to Commons., Public Domain, https://commons.wikimedia.org/w/index.php?curid=1715297

## Slide 54: Effects of orbit altitude
Van Hallen Belts extend from an altitude of about 500 to 58,000 kilometers above the surface in which region radiation levels vary.
By Booyabazooka at English Wikipedia - Transferred from en.wikipedia to Commons., Public Domain, https://commons.wikimedia.org/w/index.php?curid=1715297

## Slide 55: Effects of orbit altitude
By trapping the solar wind, the magnetic field deflects those energetic particles and protects the Earth's atmosphere from destruction.
The belts trap energetic electrons and protons. Other nuclei (e.g. alpha particles) are less prevalent.
BUT…
The belts endanger satellites, which must have their sensitive components protected with adequate shielding if they spend significant time in that zone.

## Slide 56: Effects of orbit altitude

## Slide 57: Spacecraft Localization
NORAD (North American Aerospace Defense Command)
Tracks (by radar) every object in space every few days
Returns «TLEs» containing measured orbital parameters

## Slide 58: Spacecraft Localization
From measured orbital parameters each spacecraft shall predict orbit for the following days until next NORAD update
NORAD
GROUND STATION
CONTROL CENTER
SPACE CRAFT
ON-BOARD
PREDICTOR

## Slide 59: PART II
Spacecraft Attitude

## Slide 60: Reference Frames
Z=Earth Rotation Axis
X=Vernal Point
Orthogonal
Earth-Centered Inertial Frame (ECI)
XY plane is equatore

## Slide 61: Reference Frames
O is C.O.G.
Sat-Centered Inertial Frame (SCI)

## Slide 62: Reference Frames
is nadir
O’ is C.O.G.
is orthogonal to orbit
Orthogonal
Orbital Frame
(not very useful for us…)

## Slide 63: Reference Frames
O is C.O.G.
Orthogonal
Z may be heading direction for telescope
may be antenna principal direction.
Must be normal to
Body-Fixed Frame
, , are pre-defined relevant directions for spacecraft

## Slide 64: Reference Frames
O’ is C.O.G.
is parallel to equator
Z always aims at desired target
Orthogonal
Target-Pointing Frame

## Slide 65: Reference Frames
ECI + Sat-Centered

## Slide 66: Reference Frames
ECI + Orbit

## Slide 67: Reference Frames
ECI + Body-Fixed

## Slide 68: Reference Frames
All frames…

## Slide 69: Attitude
Spacecraft Attitude is defined as the ROTATION from
Spacecraft Centered Inertial Frame to
Body-Fixed Frame
We have to define rotations (attitudes et al.) mathematically:
Euler Angles
Axis + Angle
Rotation Matrix
Quaternion

## Slide 70: Euler Angles
ANY orientation can be achieved by composing three elemental rotations, i.e. rotations about the axes of a coordinate system.
Euler angles can be defined by three of these rotations.

## Slide 71: Euler Angles
Euler angles:
z-x-z
Other Euler angles are:
x-y-x
y-z-y
z-y-z
x-z-x
y-x-y
By Euler2.gif: Juansemperederivative work: Xavax - This file was derived from Euler2.gif:, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=24338647
Z
X
Y

## Slide 72: Axis + Angle
Euler's rotation theorem states that, in 3-D, any displacement of a rigid body such that a point on the rigid body remains fixed (C.O.G. in our case),
is equivalent to
a single rotation by some angle about some axis that runs through the fixed point.
It also states that the composition of two rotations around the same point (C.O.G. in our case) is also a rotation.

## Slide 73: Axis + Angle
By DF Malan - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=1354297

## Slide 74: Rotation Matrix
Orthogonal axes (e.g. Sat-Centered Inertial) can be expressed as 3-D vectors:
Or, altogether, as a matrix:

## Slide 75: Rotation Matrix
Axes are mutually orthogonal as their mutial dot products are null:
Axes are also unit-length as their norm is unity:

## Slide 76: Rotation Matrix
Axes of rotated frames X’Y’Z’ (e.g. Body-Fixed) can also be expressed as three 3-D vectors.
For instance:
Or again as a matrix:

## Slide 77: Rotation Matrix

## Slide 78: Rotation Matrix
Axes are again mutually orthogonal as their dot products are null:
Axes are also unit-length as their norm is unity:
Try yourself if you do not believe…

## Slide 79: Rotation Matrix
A rotation matrix can be derived from rotation axis + angle. From Wikipedia:
Viceversa (from rotation matrix to axis + angle):
rotation axis is the only non-complex eigenvector of the rotation matrix

## Slide 80: Quaternion
A quaternion is a more compact expression of a rotation. It is totally equivalent to a rotation axis + angle.
In mathematics, the quaternions are a number system that extends the complex numbers.
Quaternions are represented in the form:
where a, b, c, and d are real numbers, and i, j, k are the fundamental quaternion units

## Slide 81: Quaternion
Given a rotation axis and an angle
, such that
The corresponding quaternion is defined as:

## Slide 82: Quaternion
Or, in vector form:
consequently
Conversion to/from quaternion and axis+angle is immediate
Conversion to/from quaternion and rotation matrix is similar to conversion between rotation matrix and axis+angle (already seen)

## Slide 83: Degrees Of Freedom
In physics, the Degree Of Freedom (DOF) of a mechanical system is the number of independent parameters that define its configuration.
For instance:
A point in 3-D has three DOF (its three coordinates)
A point on a sphere has two DOF (either longitude/latitude or azimut/elevation)
An axis has two DOF (azimut/elevation)

## Slide 84: Degrees Of Freedom
A unit-length vector has two DOF (the third coordinate is obtained by constraint )
A rotation has three DOF (axis (2) + angle (1))
A quaternion has three DOF (4 components – 1 constraint )
A rotation matrix has three DOF:
  first 2 coord. of ; third one comes from ;
  first coord. of ; 2nd and 3rd come from and ;
  remaining three coord. of come from , , !!!

## Slide 85: Inverse Rotation
Inverting rotation, with:
Euler angles: invert angles and invert sequence:
Rotation matrix: invert matrix (or transpose!)
=

## Slide 86: Inverse Rotation
Inverting rotation, with:
Axis and rotation: same axis, opposite angle
Quaternions: invert non-real components

## Slide 87: Combining Rotations
When a rigid body is first rotated by rotation matrix then by another rotation then by a third one , rotation can be combined by multiplying matrices:

## Slide 88: Combining Rotations
Matrix multiplication is NOT commutative, so:
That is, inverting the sequence of rotations leads to a different rotation!!!

## Slide 89: Combining Rotations
Now try to compute corresponding matrices…

## Slide 90: Spin
When rotation of a rigid body is continuous, the problem may become quite complex.
A particular and easy situation is when the rotation axis remains constant, while rotation angle continuously varies at a constant rate
In this case rotation is called «spin» and is expressed by a vector
Namely, a vector in the direction of of amplitude (NOT and axis + angle !!!)

## Slide 91: Esercizio 1
Tre rotazioni successive (NON angoli di Eulero):
  90° intorno a Z
  90° intorno a Y’
  90° intorno a X’’
Trovare asse + angolo
?

## Slide 92
Soluzione 1

## Slide 93: Esercizio 2
Tre rotazioni successive (NON angoli di Eulero):
  90° intorno a Y
  90° intorno a Z’
  90° intorno a X’’
Trovare asse + angolo
?

## Slide 94
Soluzione 2

## Slide 95: Passaggi 1) + 2):
Trovare asse + angolo
?

## Slide 96: Soluzione
Angolo: 240°, -240° (480°) per la permutazione successiva

## Slide 97: Esercizio 3
Trovare gli angoli di Eulero per la rotazione in figura:
Trovare asse + angolo
?

## Slide 98
Soluzione 3
1) +90° intorno Z’’
2) +90 intorno X’
3) -90° intorno Z

## Slide 99: Reference Frames
We will mostly use the following frames:
Sat-Centered Inertial (the reference)
Body-Fixed
Target-Pointing

## Slide 100: An Exercise - I
Given spacecraft COG located at longitude 35°, latitude 22°25’12" and altitude 600km above sea level (longitude from Vernal point)
Given mission pointing target on Earth at longitude 34°12’02", latitude 21°12’ (sea level)
Compute axis of Target-Pointing Frame (from COG to target)
Compute axis of Target-Pointing Frame (orthogonal to and parallel to equator)
Compute axis of Target-Pointing Frame (ortogonal to both and )

## Slide 101: Answers - I
TWO solutions:
Alternatively
Same Z. Opposite X and Y

## Slide 102: An Exercise - II
Given spacecraft COG located at longitude 35°, latitude 22°25’12" and altitude 600km
Given mission pointing target in deep space at azimut 12°10’22" (w.r.t. Vernal point), elevation -15°10’ (w.r.t. equatore)
Compute axis of Target-Pointing Frame (from COG to target)
Compute axis of Target-Pointing Frame (orthogonal to and parallel to equatore)
Compute axis of Target-Pointing Frame (ortogonal to both and )

## Slide 103: Answers - II
TWO solutions:
Alternatively
Same Z. Opposite X and Y
Why TWO?

## Slide 104: Comment to Exercise
Aim of your attitude control system shall be to rotate spacecraft such that its Body-Fixed Frame coincides with Target-Pointing Frame…
That is, find a rotation such that:
Therefore:
GREAT!
Seems simple…
BUT

## Slide 105: Comment to Exercise
Since is known (mission dependent), two questions arise:
How to measure ?  Attitude Determination
How to rotate by ?  Attitude Control

## Slide 106: Attitude Determination
Aim of attitude determination system is to find the attitude of spacecraft at any given instant!
HOW?
Let’s try a simple experiment together…
We need a volunteer!

## Slide 107: PART III
Attitude Sensors

## Slide 108: Attitude Determination
The attitude of a spacecraft is defined as the ROTATION from
Spacecraft Centered Inertial Frame to
Body-Fixed Frame
to

## Slide 109: Attitude Determination

## Slide 110: Attitude Determination
The attitude of a spacecraft has three DOF!
So you need at least three independent oriented measurements, as orthogonal as possible. BUT…
The more measurements you have, the higher the accuracy
The more measurements you have, the higher is also the tolerance to faults
Let’s first have a look at the existing attitude sensors, then we will draw some consideration

## Slide 111: Attitude Determination
What can you measure in a S/C for attitude?
Earth magnetic field (axis of magnetic field  2 DOF; oriented)
Sun light (axis of luminous radiation  2 DOF; oriented) – only during day 60-70% of time…
Ground station RF (axis of RF signal  2 DOF; often UN-oriented) – only during TX
Star pattern (axis of pointing vector  2 DOF; plus angle  1 DOF)
Ground photos (axis of pointing vector  2 DOF; plus angle  1 DOF)

## Slide 112: Spin Determination
What can you measure in a S/C for spin?
Spin can be determined in a blind manner (no external source is required) by means of gyroscopes
Alternatively, spin can be determined by time-derivative of attitude angle

## Slide 113: Magnetometers
Different types:
Scalar (only measure total strength of field; not useful)
Vector (measure the component(s) of the magnetic field in one (or more) particular direction/s)  they measure magnetic field axis and its amplitude (not useful)

## Slide 114: Vector Magnetometers
Different types:
Rotating Coil: magnetic field induces a sine wave in a rotating coil. Phase of sinewave indicates direction but only on a 2D plane. Obsolete and mechanically complex!
Hall Effect: produce a voltage proportional to the applied magnetic field along a 1D direction. Field strength must be large, therefore not always applicable

## Slide 115: Vector Magnetometers
Magnetoresistive: thin strips of permalloy (NiFe magnetic film) whose electrical resistance varies with magnetic field.
They have a well-defined axis of sensitivity, can be produced in 3-D versions and can be mass-produced as an integrated circuit.
Response time of less than 1 microsecond and can be sampled up to 1,000 times/second.
Can have accuracy or 0.1°-1°

## Slide 116: Vector Magnetometers
Fluxgate: a small, magnetically susceptible core wrapped by two coils of wire.
An alternating current is flown in one coil, driving the core through alternating saturation.
This field induces a voltage in the second coil, which is measured by a detector.
When the core is exposed to a magnetic field, it is more easily saturated in alignment with the field and less easily in opposition to it.
The alternating magnetic field and the induced voltage go out of phase w.r.t. input current.

## Slide 117: Fluxgate Sensor
By User:Zhatt - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=280053

## Slide 118: Magnetoresistive Sensor, Bridge
HMC1051/HMC1052L/HMC1053

## Slide 119: Magnetoresistive Sensor, Bridge

## Slide 120: Magnetoresistive Sensor, Bridge
SET/RESET STRAP
The set/reset strap is spiral of metallization that couples to the sensor elements. Each set/reset strap has a resistance of a few ohms with a minimum required peak current of 400mA (pulses).
With rare exception, the set/reset strap must be used to periodically condition the magnetic domains of the magneto-resistive elements for best and reliable performance.
Periodical short pulses of high current

## Slide 121: Magnetoresistive Sensor, Bridge

## Slide 122: Magnetoresistive Sensor, Bridge

## Slide 123: Magnetoresistive Sensor, Bridge
GROUND CALIBRATION is required!
SET/RESET in flight is required!
IN-FLIGHT CALIBRATION is required!

## Slide 124: Magnetoresistive Sensor, I2C
MMC5883MA

## Slide 125: Magnetoresistive Sensor, I2C

## Slide 126: Magnetoresistive Sensor, I2C

## Slide 127: Magnetoresistive Sensor, I2C
Simpler circuit
More complex SW (configuration, readout, UART, etc.)
GROUND CALIBRATION is required!
SET/RESET in flight is required!
IN-FLIGHT CALIBRATION is required!
DIGITAL SYSTEM: may suffer from radiation-induced latchup (SEL) and upsets (SEU)

## Slide 128: IMU (Magnetometer+Gyroscope)
ICM-20948

## Slide 129: IMU (Magnetometer+Gyroscope)
ICM-20948

## Slide 130: IMU (Magnetometer+Gyroscope)

## Slide 131: IMU (Magnetometer+Gyroscope)

## Slide 132: IMU (Magnetometer+Gyroscope)

## Slide 133: IMU (Magnetometer+Gyroscope)
Very Simple circuit
Complex SW (configuration, readout, UART, etc.)
GROUND CALIBRATION is required!
IN-FLIGHT CALIBRATION is required!
DIGITAL SYSTEM: may suffer from radiation-induced latchup (SEL) and upsets (SEU)
NO FLIGHT HERITAGE

## Slide 134: Sun and Star Sensors
Different types:
Solar 1D (scalar)
Solar 2D (axis, no angle)
Solar + Horizon 3D (axis + angle)
Star 3D (axis + angle)
Note that they ALL have to identify the so-called sun poiting vector , which is by definition a unit-length vector pointing from satellite to the sun.
A unit-length vector only has two DOF, therefore two components are usually enough to define it.

## Slide 135: Solar 1D sensor
Usually made of a single photodiode foreseen for high illuminance (up to 128 k lx = 1360W/m2)
In theory current generated by the photodiode is proportional to:
Cosine of incidence angle (variable)
Illuminance (constant = 128 k lx)
Sensor sensitive area (constant)
Sensor sensitivity (constant)
Therefore
With being an appropriate constant

## Slide 136: Solar 1D sensor
CPC1822

## Slide 137: Solar 1D sensor
In theory output current is proportional to , therefore to the component of sun pointing vector (suppose that is the axis orthogonal to the sensor surface)
In practice, sensor sensitivity is not uniform in all directions therefore output is not exactly proportional to , therefore to
Must be compensated
real

## Slide 138: Solar 1D sensor
Alternatively one can use a diffusing filter in front of the sensor
SENSOR
FILTER

## Slide 139: Solar 2D sensor
Usually made of a pinhole in front of a camera.
Pinhole receives a spot of light which is offset (along and coordinates) by an amount proportional to the and components of sun point vector .
Solar 2D Sensor can either be:

## Slide 140: Solar 2D sensor
Analog: a rectangular layer of photosensitive material which distributes current onto four electrodes at the four side of the sensor. Two currents (either single-ended or differential) provide and components of sun pointing vector :

## Slide 141: Solar 2D sensor
Digital: a complete bitmap camera (either CMOS or CCD) which «takes a picture of the sun». A trivial piece of SW on a uC computes the X-Y coordinates of the sun center, which are a measure of the and components of sun pointing vector :

## Slide 142: Other attitude sensors
RF Direction Of Arrival (DOA) sensors: an antenna array together with some RF phase measurement circuits.
It measures the direction of arrival of RF signals from ground station and computes the and components of ground-station pointing vector :

## Slide 143: Other attitude sensors
Star Sensor: a complete optical system made of a high aperture lens plus a bitmap camera (either CMOS or CCD) which takes a picture of the stars in the sky.
A non-trivial piece of SW on a uC identifies the most brilliant stars in the scene and locates them in a detailed sky map stored on-board.
Usually three to five stars are enough to locate their position in the sky map.

## Slide 144: Other attitude sensors
SKY MAP
CAMERA

## Slide 145: Other attitude sensors
A star sensor computes the X-Y coordinates of the star pointing vector :
In addition (it is the only sensor which can do it!) it computes the angle of rotation around star pointing vector, deriving the angle from the rotation of the camera scene w.r.t. the sky map!

## Slide 146: Summing Up…
All attitude sensors measure one or more components (e.g. , , ) of a given axis (either magnetic field or sun pointing or RF direction or star direction ) w.r.t. the Body-Fixed Reference Frame
Next step will be to merge all measurements together to retrieve some useful information out of them (not so easy, maybe…)
Are you sure???

## Slide 147: Major Sources of Error
Most sensors suffer from one or more:
Gain (sensit.) Error
Gain Drift with temperature or aging
Offset
Offset Drift with temperature or aging
Misalignment (cross-axis)
Misalignment Drift (usually negligible)
Noise + INTERFERENCES!!!
Occasional Failures (e.g. SEL/SEU)
Permanent Failures (e.g. broken wire)
GROUND CALIBRATION
IN-FLIGHT CALIBRATION
SUPERVISION

## Slide 148: Major Sources of Error
Gain Errors:
Transducer sensitivity
Conditioning Electronic tolerances
Perturbing external elements (e.g. metallic elements, reflecting surfaces)
Temperature drifts
Aging
Supply voltage sensitivity
TYPICAL VALUES: 1%-10%

## Slide 149: Major Sources of Error
Offset Errors:
Transducer offset
Conditioning Electronic offset
Perturbing external elements (e.g. magnetic elements; e.g. magnetorquers with iron core!)
Temperature drifts
Aging
Supply voltage sensitivity
TYPICAL VALUES: +/- 5%-50% FS !!!

## Slide 150: Major Sources of Error
Misalignments:
Transducer instrinsic misalignment
Perturbing external elements (e.g. metallic elements)
Assembly misalignment (+/- 0.2mm soldering tolerance over 10mm package width  5.7° )
TYPICAL VALUES: 1° - 10°

## Slide 151: Major Sources of Error
INTERFERENCES. Just a few examples for magnetometers:
An unshielded power supply PCB track conducting 1A generates, at 5cm distance (half the size of a 1U CubeSat) a field of 0.04G = 4.000 nT = 10% of max Earth field!!!
If the distance is 1cm, the field is 0.2G !!!
A magnetorquer (suppose 0.2A in 200 coils of 8cm diameter) generates a field of 890,000 nT (15 times max Earth field!!!)
An iron screw close to magnetometer…

## Slide 152: Homogeneous Sensor Fusion
Imagine a «real» situation…

## Slide 153: Homogeneous Sensor Fusion
How can you combine all measurements from several HOMOGENEOUS sensors (e.g. all the magnetic)?
Remember that the more sensors you have, the safer is the system in case of failures!!!
… and individual errors tend to compensate!!!
But each sensor may have its own: Orientation, Misalignment, Gain, Offset…

## Slide 154: Homogeneous Sensor Fusion
Given magnetic field expressed as a vector in the body-fixed frame
Each -th sensor will respond accordingly, providing ONE output
Consider 2D/3D sensors as 2/3 independent
For each sensor, its will depend on its orientation, alignment, gain, offset , noise :
where

## Slide 155: Homogeneous Sensor Fusion
Each (respectively, and ) is the response of the sensor to a magnetic field oriented along (respectively, and ) axis in the body-fixed frame
Therefore
means:

## Slide 156: Homogeneous Sensor Fusion
By putting all and as rows of two matrices
By multiplying, we get a column vector of the responses from all homogeneous sensors:

## Slide 157: Homogeneous Sensor Fusion
The problem is now:
If all and are known (reasonable)
Supposing noise random
Given the set of measured values
What is the most likely value of ?
From
If we neglect noise , then

## Slide 158: Homogeneous Sensor Fusion
When is not square (more equations than unknowns) we use the «left division» or «pseudoinverse» instead. Either:
where \ is left division and is pseudo-inverse (SEE Wikipedia for definitions…)

## Slide 159: Homogeneous Sensor Fusion
Since:
All and are known
Given the set of measured values
Having found the most likely value of
From
In theory
But, due to error, noise, faults, one or more components might not match

## Slide 160: Homogeneous Sensor Fusion
Try to identify qhat componet does not match and act accordingly (correct G, O or flag the sensor as faulty…)

## Slide 161: Homogeneous Sensor Fusion

## Slide 162: An Exercise - III
Imagine the small-sat in figure:
The top frame is Body-Fixed
Y axis is aligned with major diagonal
The other frames are the X-Y-Z coordinates of as many 3D magnetometers
The leftmost has X axis offset by 20 degrees w.r.t. sat X
Red is always X, Green is always Y, Blue is always Z

## Slide 163: An Exercise - III
Suppose magnetometer sensitivity between 40000 and 50000 V/T (random)
Suppose offsets between -0.5V and + 0.5V (random)
Compute matrices and
Suppose magnetic field of (-0.15, +0.02, 0.22) G
Compute expected sensor outputs
Add noise with variance 0.05V to outputs
Given these values compute  compare

## Slide 164: PART IV
Attitude Determination

## Slide 165: Heterogeneous Sensor Fusion
Suppose a number of «axes» have been identified, from individual homogeneous sensor fusions. For instance:
is the measured magnetic field
is the measured sun pointing vector
is the measured RF direction
Each of them may have a different reliability:
is the reliability of magnetic measurement
is the reliability of sun measurement
is the reliability of RF measurement

## Slide 166: Heterogeneous Sensor Fusion
We have now to identify spacecraft attitude w.r.t. sat-centered inertial frame :

## Slide 167: Heterogeneous Sensor Fusion
In practice, the measured «axes» in frame

## Slide 168: Heterogeneous Sensor Fusion
Are THE SAME PHISICAL PARAMETERS which exist in frame

## Slide 169: Heterogeneous Sensor Fusion
Except for the same (inverse) rotation
RGB is sat
Black are measurements

## Slide 170: Heterogeneous Sensor Fusion
Therefore inverse rotation is the one which:
Rotates back into
Rotates measured values back into real physical parameters

## Slide 171: Heterogeneous Sensor Fusion
We must therefore know:
Real magnetic field in frame :
  Depends on orbit point (see part I)
  Requires mathematical model of geomagnetic field (known, from the web)
Real sun pointing vector in frame :
  Requires well-known orbital parameters of sun (known, from astronomy)
Real RF pointing vector in frame :
  Depends on orbit point (see part I)
  Depends on location of ground station
Etc.

## Slide 172: Heterogeneous Sensor Fusion
We have measured:
Estimated magnetic field in frame from sensor fusion
Estimated sun pointing vector in frame from sensor fusion
Estimated RF pointing vector in frame from sensor fusion
Etc.

## Slide 173: Heterogeneous Sensor Fusion
In theory, if:
Then:
Therefore, in theory:
From which:

## Slide 174: Heterogeneous Sensor Fusion
In practice, because of measurement errors the matrix R is not a mathematically correct rotation matrix!!!!.
We have to slightly modify the method…
Let’s try to identify two formally correct reference frames strongly related with the measured parameters () and the real physical parameters ()
What is a formally correct reference frame ???
ORTHOGONAL and UNIT LENGTH

## Slide 175: Heterogeneous Sensor Fusion
First axis of : the more reliable measurement in frame (e.g. ) made with unit length:
First axis of : the corresponding real physical value in frame (e.g. ) made with unit length:

## Slide 176: Heterogeneous Sensor Fusion
Second axis of : an axis orthogonal to the two measurements (for more than two it is slightly more complex) made with unit length:
Second axis of : the same in frame :

## Slide 177: Heterogeneous Sensor Fusion
Third axis of : must be orthogonal to the other axes and unit-length:
Third axis of : the same in frame :

## Slide 178: Heterogeneous Sensor Fusion
Now apply the formula found before to these formally correct frames:
And the matrix turns out to be correct (proof omitted…)
As already said, if you have more than two physical parameters, the method is similar but a few additional steps are required (omitted here)

## Slide 179: Heterogeneous Sensor Fusion
Partial conclusion:
We have been able to find spacecraft attitude !!!!
We can therefore estimate rotation to achieve desired mission target
Now still the last step…

## Slide 180: PART V
Attitude Actuators

## Slide 181: Spin
When rotation of a rigid body is continuous, the problem may become quite complex.
A particular and easy situation is when the rotation axis remains constant, while rotation angle continuously varies at a constant rate
In this case rotation is called «spin» and is expressed by a vector
Namely, a vector in the direction of of amplitude (NOT and axis + angle !!!)

## Slide 182: Spin
By DF Malan - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=1354297
Ω

## Slide 183: Axis + Angle
By DF Malan - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=1354297

## Slide 184: Rotation by angle
ω
θ
Δω
-Δω

## Slide 185: Attitude Actuators
Rotations around C.O.G. require a pair of identical forces, called torque C
: no acceleration of C.O.G.
Torque
F
F
d

## Slide 186: Propulsion
Problem: we have to apply a . How ?
Newton’s laws applied to rotation:
Preservation of momentum: if : = const if : … = const if : = 0
Torque Impulse: if we apply for :

## Slide 187: Attitude Actuators
A torque can be generated more easily than a single force! Three major techniques:
Mechanically, by using the principles of conservation of angular momentum (e.g. reaction or momentum wheels)
Magnetically, by using interaction between an internally generated magnetic field and the Earth magnetic field (magnetorquers)
By means of a pair of thrusters in opposite directions

## Slide 188: Attitude Actuators
Rotations around C.O.G. require pairs of forces.

## Slide 189: Momentum Actuators
A momentum actuator is based on the principles of preservation of the angular momentum.
In a closed system (a spacecraft) made of two parts (bus+payload and momentum actuator), the sum of angular momenta is constant.
Therefore
Or, equivalently

## Slide 190: Momentum Actuators
Where
is the angular momentum of a body and is the product of its inertia tensor (matrix) and its angular velocity .
A reaction wheel generates internally an angular momentum by means of:
a motor spinning at speed
a mass of inertia

## Slide 191: Momentum Actuators

## Slide 192: Momentum Actuators
Consequently the spacecraft will acquire the opposite momentum
Therefore a spin variation

## Slide 193: Momentum Actuators
Orbital manoeuvres:
Spining/despinning: the motor must maintain a given velocity to allow spacecraft to achieve a given . E.g. to despin from an initial spin to 0, or from an initial null spin to a desired spin
Rotation: the motor must rotate a given additional angle to rotate spacecraft by an angle . E.g. to aim to a desired target (required rotation )

## Slide 194: Momentum Actuators
Mind that if the motor was rotating at an initial velocity this corresponds to an acceleration and deceleration for a given time
Compensating external torques (e.g. solar pressure on non uniform lateral surfaces). This requires an acceleration that is, an ever increasing angular acceleration which will soon drive motor/ wheel to saturate to its maximum speed!!!

## Slide 195: Momentum Actuators
Advantages:
Very fast and easy to control
Drawbacks:
Motor shall continuously dissipate power to maintain its spin
Saturation: sooner or later the wheel saturates and requires desaturation (transfer of its angular momentum to another attitude actuator

## Slide 196: Magnetic Actuators
A magnetic actuator is based on the magnetic interaction between an internally generated magnetic momentum and the Earth (or other planet) magnetic field .
is perpendicular to both and

## Slide 197: Magnetic Actuators
A magnetic actuator can be made of either:
A magnet, having its constant momentum (trivial solution; cannot be controlled)
A flat solenoid
A cylindrical solenoid

## Slide 198: Magnetic Actuators
Magnetic actuators can also be embedded inside other spacecraft systems

## Slide 199: Magnetic Actuators
Magnetic momentum of a flat solenoid is given by:
where:
is number of turns
is solenoid current
is coil area
is normal to coil

## Slide 200: Momentum Actuators
Advantages:
Many manoeuvres require limited power
Can be used to desaturate reqction wheels
Drawbacks:
Slower than reaction wheels
Torque only perpendicular to the magnetic field. No torque parallel to it is achievable
Their control is more comples
Cannot be used in deep space or around plantes with no magnetic field

## Slide 201: PART VI
Magnetic Attitude Control

## Slide 202: Magnetic Attitude Control
How can we use magnetic actuators to generate either:
A given spin
A rotation matrix
Since the achievable magnetic torque can only be orthogonal to magnetic field???

## Slide 203: Magnetic Attitude Control

## Slide 204: Magnetic Attitude Control
A few considerations:
Generic manoeuvres are not achievable magnetically unless one can allow enough time to complete them.
Only manoeuvres orthogonal to magnetic field can be implemented.
If you have them, angular manoeuvres () are easier, faster and less power consuming with reaction wheels
If you have no reaction wheel, one shall accept longer manoeuvre time

## Slide 205: Magnetic Attitude Control
Spin manoeuvres are better implemented with magnetorquers, unless they have to be fast
As a rule of thumb, generic manoeuvres require, in the worst case, from a quarter to half an orbit to be completed
The question is now: how to plan actuation commands along the orbit, to achieve a desired ?
Angular manoeuvres are split into three phases: (  rotation  )

## Slide 206: Magnetic Attitude Control
Magnetic actuators produce a torque which causes an angular acceleration:
If we consider a short period in which acceleration remains constant:
We can split the manoeuvres time into a sequence of identical time intervals:

## Slide 207: Magnetic Attitude Control
Magnetic actuators produce a torque which causes an angular acceleration:
If we consider a short period in which acceleration remains constant:
We can split the manoeuvres time into a sequence of identical time intervals:

## Slide 208: Magnetic Attitude Control
T1a
T1b
T2a
T2b
Tja
Tjb

## Slide 209: Magnetic Attitude Control
Where
We can create a matrix

## Slide 210: Magnetic Attitude Control
The eigenvectors of the inertia matrix are called principal axes.
Let’s suppose now for simplicity that the principal axes are parallel to the body-fixed frame , which is a simplified situation.
In this case inertial is a diagonal matrix

## Slide 211: Energy for Attitude Determination
Spacecraft is spinning at rate ω (rad/s or PRM):
If we sample attitude every (s), attitude angle varies by an angle
From one sample to the next one;
The indetermination of attitude angle due to sampling is therefore

## Slide 212: Energy for Attitude Determination
Each individual measurement requires a power for a minimum measurement time of therefore an energy of
Acrtivating, measuring and deactivating an attitude sensor for the minimum measurement time at a rate of samples/s requires and average power of

## Slide 213: Energy for Attitude Control
xxx

## Slide 214: Rotazione
v(m/s)
t(s)
A
C
B
F(N)
Consumo
(%)
acc
acc
moto uniforme
moto uniforme
dec
dec

## Slide 215: Spostamento Rapido
v(m/s)
t(s)
A
C
B
F(N)
Consumo
(%)
C
B

## Slide 216: PART VII
Attitude and Orbit Codetermination

## Slide 217: PART VIII
POLITO-SATC achievements

## Slide 218: ULTRA-THIN Reaction wheel
Notes: Manca:
3d della ruota;
ipertesto performance.

## Slide 219
COTS (3.5” hard disk plate, low cost)
Ultra-thin (4.7-6 mm)
Light (165-190 g)
Flexible (larger/smaller scale)
ULTRA-THIN Reaction wheel

## Slide 220: AraMiS CubeSats - Aramis C1

## Slide 221: AraMiS Missions – AraMiS – RW1

## Slide 222: AraMiS Missions – AIM1 (telescope)
Exploded view
9cm reflector telescope

## Slide 223: AraMiS Missions – AIM2 (LIBS)
Exploded view
LIBS (Laser-Induced Breakdown Spectrometer)

## Slide 224: AraMiS Missions – multi-payload