## Slide 1: Design optimization of CubeSat telescopes and imagers for Earth and space observation
APSCO - 2019
Leonardo M. Reyneri
Politecnico di Torino

## Slide 2
TERMINOLOGY

## Slide 3: What is a Telescope ?
An optical instrument to see “far away” with a sufficient resolution within a sufficient field of view…

## Slide 4: Zeiss-Gautier Ground Telescope

## Slide 5: Space Telescope
A space telescope is an optical device made of four major elements:
The optical system (made of lenses and mirrors)
A mechanical structure
An optoelectronic detector (other detectors are ruled out in space!)
The target!

## Slide 6: Reasons for Space Telescopes
No atmosphere! Therefore:
No light dispersion
No light pollution
No selective absorbance
No distorsion

## Slide 7: Reasons for Space Telescopes
Selective absorbance of atmosphere

## Slide 8: Reasons for Space Telescopes
Light pollution and dispersion
New York
Paris
City
Small Village

## Slide 9: Reasons for Space Telescopes
Atmosphere refraction and distorsion
Moon

## Slide 10: AraMiS Missions – AIM1 (telescope)
Hubble Space Telescope

## Slide 11: AraMiS Missions – AIM1 (telescope)
Exploded view
9cm reflector telescope

## Slide 12: Field of View
The Field of view (FOV)
is the open observable area a person can see through eyes or via an optical device.
In the case of optical devices and sensors, FOV describes the angle through which the telescope can pick up electromagnetic radiation (light).
FOV of human eye is about 210x150 deg

## Slide 13: Field of View
Field of View = ANGLE

## Slide 14: Zenith and Nadir
The nadir is the direction pointing directly “below” a particular location; namely, one of the two vertical directions at a specified location.
In space, the concept of “being below” is vague  in astronomy the nadir is the direction of the force of gravity at a given location.
The direction opposite of the nadir is the zenith.
In deep space there is neither nadir nor zenith!

## Slide 15: Zenith and Nadir

## Slide 16: Zenith and Nadir
NADIR
ZENITH

## Slide 17: Ground Footprint
Field of view (FOV) is an angle. That’s ok when talking about viewing stars or small bodies (e.g. a planet from far away).
When viewing at a larger celestial body (e.g. the Earth from an Earth orbit or the Moon from a Moon orbit), FOV spans an area on the ground called ground footprint.

## Slide 18: Ground Footprint
Ground Footprint = AREA

## Slide 19: Ground Footprint
Ground Footprint
(100km x 100km)
Field of View
(20° x 20°)

## Slide 20: Telescope – Optical System
The optical system of a telescope is made of one or more lenses or mirrors placed at a certain, fixed distance from each other.
Three types:
Refracting, using only lenses
Reflecting, using only mirrors
Catadioptric, using both mirrors and lenses
Pinholes, using neither of them

## Slide 21: Refracting - Lens Principle

## Slide 22: Lens Principle – Positive Lens

## Slide 23: Lens Principle

## Slide 24: Lens Principle - Negative Lense

## Slide 25: Lens Principle

## Slide 26: Focal Length
In vacuum, glass lens ():
In air ():

## Slide 27: Focal Length
An example:
(glass)
In vacuum ():
In air ():
 !!!

## Slide 28: Lens operation – close distance
Lens center
Focal point
Focal point
Target
Real Image

## Slide 29: Lens operation – variable distance
The relationship between target distance , focal length and position of projected image is given by:
 target and image same size
  target at infinity, image in focal plane

## Slide 30: Lens operation – infinite distance
Focal plane

Focal point
Lens center


## Slide 31: Lens operation – infinite distance
Focal plane

Lens center


## Slide 32: Lens operation – infinite distance
Position on detector surface of targets located at infinite distance is proportional to incident light beam angle

## Slide 33: Earth (Moon) images

## Slide 34: Sky images

## Slide 35: Refracting Telescope for eye

## Slide 36: Refracting Telescope for space

## Slide 37: Reflecting – Mirror Principle

## Slide 38: Reflecting – Mirror Principle

## Slide 39: Focal Length
For a mirror, focal length is simple…

## Slide 40: Mirror operation – variable distance
The relationship between target distance , focal length and position of projected image is given by:
 target and image same size
  target at infinity, image in focal plane

## Slide 41: Optical Configurations
In principle, detector must be placed on focal plane.
Both lens/mirror and detector must be inside the same S/C
Focal length < largest S/C size !!!
There are though some optical configurations which allow to have longer focal lengths than S/C size. Most of them are for mirrors, but you can also use them with lenses

## Slide 42: Optical Configurations
Galileo (only for human eye)

## Slide 43: Optical Configurations
Reflecting
DETECTOR
SPACECRAFT

## Slide 44: Optical Configurations
Gregory
DETECTOR
SPACECRAFT

## Slide 45: Optical Configurations
Cassegrain
DETECTOR
SPACECRAFT

## Slide 46: Optical Configurations
Gregory
DETECTOR
SPACECRAFT

## Slide 47: Angular Resolution
Angular resolution is (roughly) the smallest angular distance (in degrees or radians) between two bright points which allows to distinguish them from each other.
θR

## Slide 48: Angular Resolution
Two points closer than the angular resolution are perceived as being a single (unfocused) point.
Angular resolution is usually measured at the nadir, as this is the direction offering the sharpest image.
θR

## Slide 49: Ground Resolution
Ground resolution is (roughly) the smallest geometrical distance (in meters) between two bright points on the Earth (or Moon or any other planet) which allows to distinguish them from each other.
For a spacecraft orbiting at an altitude , at the nadir:

## Slide 50: Ground Resolution

## Slide 51: Two Resolutions ?
Angular resolution is adopted whenever there is no specific “distance” from the target, typically when the target is at the infinity. For instance when taking pictures of stars or planets.
Ground resolution is adopted whenever there is a specific distance from the target, typically when taking pictures of Earth or Moon or close by pictures of other planets. The distance is always measured at the zenith and coincides with the spacecraft orbiting altitude.

## Slide 52: Resolution

## Slide 53: Relative Resolution
One can define the relative resolution as the ratio between the angular/ground resolution and the field-of-view/footprint:
which roughly represents how many useful “pixels” can be extracted along each direction of the image

## Slide 54: Optical image size
The optical image size of a telescope represents the maximum number of useful pixels which can be extracted from an image provided with an ideal detector.
For a telescope with a rectangular FOV
optical image size is given by

## Slide 55: Elements Affecting Resolution
Resolution (both angular and ground) depend on:
Lens/mirror diameter
Resolution of the detector (number of pixels)
Focusing
Aberrations
Wavelength
Spin

## Slide 56: Lens/mirror Diameter
Diffraction is an optical phenomenon which takes place whenever light encounters an obstruction.
In particular when it encounters the input aperture of the telescope (or the diaphragm, if any)

## Slide 57: Diffraction
AIRY DISK
AIRY DISK

## Slide 58: Resolution due to Diffraction
AIRY DISK
D

## Slide 59: Diffraction
AIRY DISK
COLOURED!
D

## Slide 60: Small pinholes
AIRY DISK
D

## Slide 61: Detector Resolution
A “continuous” image on the focal plane is spatially sampled by an optoelectronic detector made of a large number of regularly spaced “pixels” (e.g. 512x512 pixels)

## Slide 62: Detector Resolution
Focal plane

Lens center


## Slide 63: Detector Resolution
Focal plane
«Continuous» image

## Slide 64: Detector Resolution
Focal plane

Lens center



## Slide 65: Focusing
What happens if detector is not perfectly on the focal plane ?
We talk about unfocusing

## Slide 66: Focusing
Focal plane

Detector
Detector

## Slide 67: Focusing
Focal plane
Detector

## Slide 68: Focusing

## Slide 69: Wavelength
Wavelength affects:
Refraction index of glass (only for lenses), therefore focal length
Diffraction

## Slide 70: Cromatic Aberration

## Slide 71: Cromatic Aberration
Refraction index of glass
blue
red
green
Like unfocusing

## Slide 72: Spin
Telescope spin drifts image over detector during aperture time by an angle which blurs the image impacting resolution by the same amount

## Slide 73: Aberrations
In optics, aberration is a property of optical systems such as lenses that causes light to be spread out over some region of space rather than focused to a point.
Aberrations cause the image formed by a lens to be blurred or distorted, with the nature of the distortion depending on the type of aberration.

## Slide 74: Spherical Aberration in lenses
«Focal» plane

## Slide 75: Spherical Aberration in mirrors
«Focal» plane

## Slide 76: Spherical Aberrations
Spherical Aberration in lenses is:
proportional to fourth power of diameter
inversely proportional to third power of focal length
Function of refraction index of glass
Solutions:
Aspherical lens/mirror
Combination of positive and negative lenses/mirrors

## Slide 77: Astigmatism

## Slide 78: Distorsion

## Slide 79: Elements Affecting Resolution
Field of View:
Diffraction
Detector resolution:
Unfocusing:
Cromatic:
Spin:
Other Aberrations…

## Slide 80: Relative Resolution & Image Size
Resuming:

## Slide 81: Example I
(detector, 512x512 ->
(blue)
Limited by chromatic/unfocusing!

## Slide 82: Telescope – Mechanical Structure
Mechanical structure has to:
Keep lenses/mirrors/detector in the right position
Protect optical system against dust
Protect optical system during vibrations
And MUST:
Keep focusing within less than 100µm (TBD) after vibration and over all temperature range
Keep lens/mirror/detector alignment

## Slide 83: Telescope – Optical Detector
A space telescope is an optical device made of four major elements:
The optical system (made of lenses and mirrors)
A mechanical structure
An optoelectronic detector (other detectors are ruled out!)
The target!